Submission to the New Journal of Student Research Abstracts

ExB Drift of an Argon Plasma

Roland Hwang, Max Praglin (The Buckley School, Sherman Oaks, CA), Aly Lodge, Rachel Biniaz (Archer School for Girls, Brentwood, CA), Amy Lee, Gabriela Rosales, Robin Shin (New Roads School, Santa Monica, CA), Bob Baker (University High, Los Angeles, CA), Joe Wise (New Roads School, Santa Monica, CA), Walter Gekelman, Patrick Pribyl (UCLA)

Students in the LAPTAG (Los Angeles Physics Teachers’ Alliance Group) Plasma Laboratory at UCLA measured the flow at the edges of an argon plasma due to ExB drift. ExB drift is a phenomenon that causes plasma to spiral at the edges while flowing away from the RF source. Drift was measured using a two-sided probe. Each side was a conductor hammered flat that collected argon gas as it was ionized. Depending on which way the plasma drifted, one side would collect more ions than the other and thus have a higher current when measured. After the data was taken, numbers were analyzed using IDL and the Mach number plotted. The Mach number is the ratio of velocity over the ion sound speed, which is also equivalent to the ratio of the difference of the currents divided by their average. The flow of the plasma at 80 s after the shutoff of the RF source was measured to be 1.63 x 103 m/s. From measurements of the electric field and magnetic field (measured previously using a Langmuir probe and gaussmeter), the ExB drift was predicted to be approximately 5.3 x 103 m/s. Our results agree within a factor of three, therefore this method reasonably predicts argon drift at the edges of the cylindrical plasma chamber.